## Slide 1: Wi-Fi HaLow: Enabling untethered intelligence (aka Edge AI) Andy McFarlane VP Marketing, Morse Micro

## Slide 3: The fundamentals
Edge AI is moving intelligence out of the cloud and into the world, onto devices in fields, factories, buildings, and infrastructure.
BUT
AI has a power and range problem.
The most powerful intelligence ever built, can’t ever be too far away from a wall socket.
We need a wireless layer that can reach far enough, draw little enough power, and carry enough bandwidth to support real AI workloads!

## Slide 4: How much data do you need to be intelligent?
20 B
Sensor event
Basic sensor data. Specific readings with set detail, class ID, confidence, timestamp.
200 B
Detection metadata
Multiple detected objects with class, confidence, bounding box, device ID and timestamp details.
1 KB
Feature embedding
Detection metadata plus a 512-dimension INT8 embedding, 512 bytes. Lets cloud match an scene changes across views without sending full image.
50 KB
Verification snapshot
AI triggered capture of a 640×480 JPEG on new event and passes on details to local or cloud AI review.
500 KB
Full-resolution keyframe
A 1080p JPEG or two seconds of 720p H.265.
at review quality, sent when a cloud model does the assessment and needs detailed pixels.
5 MB
Event clip or OTA update
Ten seconds of 1080p H.265 at 4 Mbit/s, including buffered pre-event footage. Also OTA model update pushed down to the device.
Example IoT device: Industrial vibration sensor
Example Edge AI device:
Kerbside parking sensor
Example Edge AI device:
Overhead occupancy sensor
Example Edge AI device:
Access control camera
Example Edge AI device:
Factory floor robots
Example Edge AI device: Site monitoring drone

## Slide 5: The key 3 for untethered intelligence

## Slide 6: Where Wi-Fi HaLow is untethering intelligence
Range
0 Mbps
10 Mbps
20 Mbps
30 Mbps
PHY throughput
100m
1 km+
200m
300m
400m
500m
600m
700m
800m
900m
40 Mbps
Wi-Fi HaLow by Morse Micro
Wi-Fi 4 / 5 / 6 / 7
Others (Bluetooth, Zigbee, Thread)
LoRa

## Slide 7: How much data do you need to be intelligent?
20 B
Sensor event
Basic sensor data. Specific readings with set detail, class ID, confidence, timestamp.
200 B
Detection metadata
Multiple detected objects with class, confidence, bounding box, device ID and timestamp details.
1 kB
Feature embedding
Detection metadata plus a 512-dimension INT8 embedding, 512 bytes. Lets cloud AI match a scene changing across views without sending full image.
50 kB
Verification snapshot
AI triggered capture of a 640×480 JPEG on new event and passes on details to local or cloud AI review.
500 kB
Full-resolution keyframe
A 1080p JPEG or two seconds of 720p H.265.
at review quality, sent when a cloud model does the assessment and needs detailed pixels.
5 MB
Event clip or OTA update
Ten seconds of 1080p H.265 at 4 Mbit/s, including buffered pre-event footage. Also OTA model update pushed down to the device.
Example IoT device: Industrial vibration sensor
Example Edge AI device:
Kerbside parking sensor
Example Edge AI device:
Overhead occupancy sensor
Example Edge AI device:
Access control camera
Example Edge AI device:
Factory floor robots
Example Edge AI device: Site monitoring drone

## Slide 8: Power consumption by packet size
Technology
200 B
Zigbee sub-GHz
LoRaWAN (SF7)
LoRa Plus FLRC
NB-IoT
1 kB
Zigbee sub-GHz
LoRaWAN (SF7)
LoRa Plus FLRC
NB-IoT
50 kB
Zigbee sub-GHz
LoRaWAN (SF7)
LoRa Plus FLRC
NB-IoT
500 kB
Zigbee sub-GHz
LoRaWAN (SF7)
LoRa Plus FLRC
NB-IoT
5 MB
Zigbee sub-GHz
LoRaWAN (SF7)
LoRa Plus FLRC
NB-IoT
Power consumption to deliver packet

## Slide 9: Power consumption by packet size
Technology
200 B
Zigbee sub-GHz
LoRaWAN (SF7)
LoRa Plus FLRC
NB-IoT
1 kB
Zigbee sub-GHz
LoRaWAN (SF7)
LoRa Plus FLRC
NB-IoT
50 kB
Zigbee sub-GHz
LoRaWAN (SF7)
LoRa Plus FLRC
NB-IoT
500 kB
Zigbee sub-GHz
LoRaWAN (SF7)
LoRa Plus FLRC
NB-IoT
5 MB
Zigbee sub-GHz
LoRaWAN (SF7)
LoRa Plus FLRC
NB-IoT
Power consumption to deliver packet
9.4 mJ
132 mJ
247 µJ
451 mJ
9.4 mJ
132 mJ
247 µJ
451 mJ
Airtime (TX)
43.8 ms
338.2 ms
655 µs
10.1 ms

## Slide 10: Power consumption by packet size
Technology
Power consumption to deliver packet
200 B
Zigbee sub-GHz
9.4 mJ
LoRaWAN (SF7)
132 mJ
LoRa Plus FLRC
247 µJ
NB-IoT
451 mJ
1 kB
Zigbee sub-GHz
47.1 mJ
LoRaWAN (SF7)
LoRa Plus FLRC
1.2 mJ
NB-IoT
475 mJ
50 kB
Zigbee sub-GHz
LoRaWAN (SF7)
LoRa Plus FLRC
60.0 mJ
NB-IoT
500 kB
Zigbee sub-GHz
LoRaWAN (SF7)
LoRa Plus FLRC
NB-IoT
5 MB
Zigbee sub-GHz
LoRaWAN (SF7)
LoRa Plus FLRC
NB-IoT
600 mJ cutoff
9.4 mJ
132 mJ
247 µJ
451 mJ
47.1 mJ
661 mJ
1.2 mJ
475 mJ
2.34 J
32.27 J
60.0 mJ
1.98 J
23.43 J
323 J
600 mJ
15.84 J
234 J
3,226 J
6 J
154 J
Airtime (TX)
43.8 ms
338.2 ms
655 µs
10.1 ms
219.2 ms
1.69 s
3.2 ms
50.6 ms
10.91 s
82.58 s
161.7 ms
2.53 s
109.02 s
825.69 s
1.62 s
25.32 s
1090.20 s
8256.57 s
16.17 s
53.16 s

## Slide 11: Power consumption by packet size
Technology
Airtime (TX)
200 B
Zigbee sub-GHz
9.4 mJ
43.8 ms
LoRaWAN (SF7)
132 mJ
338.2 ms
LoRa Plus FLRC
247 µJ
655 µs
NB-IoT
451 mJ
10.1 ms
1 kB
Zigbee sub-GHz
47.1 mJ
219.2 ms
LoRaWAN (SF7)
1.69 s
LoRa Plus FLRC
1.2 mJ
3.2 ms
NB-IoT
475 mJ
50.6 ms
50 kB
Zigbee sub-GHz
10.91 s
LoRaWAN (SF7)
82.58 s
LoRa Plus FLRC
60.0 mJ
161.7 ms
NB-IoT
2.53 s
500 kB
Zigbee sub-GHz
109.02 s
LoRaWAN (SF7)
825.69 s
LoRa Plus FLRC
1.62 s
NB-IoT
25.32 s
5 MB
Zigbee sub-GHz
1090.20 s
LoRaWAN (SF7)
8256.57 s
LoRa Plus FLRC
16.17 s
NB-IoT
53.16 s
600 mJ cutoff
9.4 mJ
132 mJ
247 µJ
451 mJ
47.1 mJ
661 mJ
1.2 mJ
475 mJ
2.34 J
32.27 J
60.0 mJ
1.98 J
23.43 J
323 J
600 mJ
15.84 J
234 J
3,226 J
6 J
154 J
Power consumption to deliver packet

## Slide 12: Power consumption by packet size
Technology
Airtime (TX)
200 B
Wi-Fi HaLow
650 µJ
320 µs
Zigbee sub-GHz
9.4 mJ
43.8 ms
LoRaWAN (SF7)
132 mJ
338.2 ms
LoRa Plus FLRC
247 µJ
655 µs
NB-IoT
451 mJ
10.1 ms
1 kB
Wi-Fi HaLow
706 µJ
480 µs
Zigbee sub-GHz
47.1 mJ
219.2 ms
LoRaWAN (SF7)
1.69 s
LoRa Plus FLRC
1.2 mJ
3.2 ms
NB-IoT
475 mJ
50.6 ms
50 kB
Wi-Fi HaLow
4.6 mJ
11.2 ms
Zigbee sub-GHz
10.91 s
LoRaWAN (SF7)
82.58 s
LoRa Plus FLRC
60.0 mJ
161.7 ms
NB-IoT
2.53 s
500 kB
Wi-Fi HaLow
40.8 mJ
111.4 ms
Zigbee sub-GHz
109.02 s
LoRaWAN (SF7)
825.69 s
LoRa Plus FLRC
1.62 s
NB-IoT
25.32 s
5 MB
Wi-Fi HaLow
404 mJ
1.11 s
Zigbee sub-GHz
1090.20 s
LoRaWAN (SF7)
8256.57 s
LoRa Plus FLRC
16.17 s
NB-IoT
53.16 s
600 mJ cutoff
650 µJ
9.4 mJ
132 mJ
247 µJ
451 mJ
706 µJ
47.1 mJ
661 mJ
1.2 mJ
475 mJ
4.6 mJ
2.34 J
32.27 J
60.0 mJ
1.98 J
40.8 mJ
23.43 J
323 J
600 mJ
15.84 J
404 mJ
234 J
3,226 J
6 J
154 J
Power consumption to deliver packet

## Slide 13: The key 3 for untethered intelligence

## Slide 14: Examples of where untethered intelligence can do better that the best current alternative
Autonomous mobile robots (AMRs)
Access control and entrance monitors
Security Cameras
Water quality monitor
Environment monitors
Crop health, pest and weed monitoring
Predictive maintenance
Autonomous AI tractors
Livestock monitors
Assisted living sensors and monitors

## Slide 15: The ChatGPT moment for physical AI is here. When machines begin to understand, reason, and act in the real world.” “
Jensen Huang
CEO, NVIDIA - CES 2026
Frontier models are extraordinary – and blind
With Wi-Fi HaLow we can now deploy it anywhere: untethered AI that sees, thinks and acts

## Slide 16: Get your hands on our dev kits!
Morse Micro’s Wi-Fi HaLow evaluation kits are available through leading electronics distributors

## Slide 17: Design Partner Program Find out more at morsemicro.com/ design-partners Join our

## Slide 18
Wi-Fi HaLow
Enabling untethered intelligence
Thank You
Notes: Maybe change the title of this slide…